## Slide 1: Finding DX {Through DX SPOTS} Phil Gould, G4FVZ

## Slide 2: What’s DX?
Acronym for long distance communication
Non-G contacts
Exotics
DXCC’s you haven’t got
Its really all relative – I’d like GI on 13cm!

## Slide 3: What’s DXCC
DX Century Club Award – 100 confirmed entities
Proof of contact – LoTW
5-Band DXCC
By mode
DXCC Country List - 338 Places

## Slide 4: If You Love Just tuning The Bands – Go Ahead
This is all about sharpening your game

## Slide 5: Before You Start – Things To Consider
HF
  Propagation
  Time of day/year – summer doldrums, grey-line
  Antennas – direction, angle of radiation
  Know where your new DXCC is
  Decide what you are hunting with – QRP or QRO
  Exploit contests – CQ WW
VHF
  Tropo, E’s, meteors, rain, aurora

## Slide 6: So What’s a Spot?
Something that helps you find the DX – someone has ‘spotted’ it
Usually delivered by a ‘Cluster’
Can be ‘Passive’ and ‘Active’

## Slide 7: Before You chase Spots Do the Simple Things
CAT control with station logger – highly desirable
  QRG, mode, beam heading
Use what the logger already provides
Remember contests - Call last, Call late
Have CW and QRO available
Major DX Expeditions on FT8
Persist

## Slide 8: Know which way you are pointing to hunt

## Slide 9: Check Out Beacons
Look up timing and frequency
For 10m and 6m use Beaconspot

## Slide 10: Let’s Get Going : Probe Band (and your Set Up) with Passive Tools
Internet scrapers
  Reverse Beacon Network (RBN)
  PSK Reporter
  Don’t forget to spot yourself

## Slide 11: Take A Look At Propagation Predictors

## Slide 12: Reverse Beacon Network (RBN)

## Slide 13: PSK Reporter : Data Modes

## Slide 14: A Lot of DX is on Digital: Understand and Use FT8 Fox & Hounds Mode
Special Operating Mode For FT8 – Dxpeditions
Identify the Fox – must use ‘split’
They may have a spot QRG low down (300-900Hz)
You are the Hound – transmit above 1000Hz
You must ‘see’ the Fox
Allows DX station to work up to 5 people at once
Remember to switch it off after!

## Slide 15: Chasing Dxpeditions : Check Their Website and Blog
Get plugged into Spot Systems that you can search by callsign:

## Slide 16: How Do You Know What’s Coming UP?

## Slide 17: Spot ‘Intelligence’ is Key

## Slide 18: DX Heat : A Good Place to Start

## Slide 19: Club Log is Really Handy

## Slide 20: DX Maps Also Useful
Search Mode, Last 15mins, propagation model

## Slide 21: DX : CLUSTER
Cluster : A DX Cluster is a means for Amateur (Ham) Radio operators to tell each other, in real time, about DX stations
Link to Logger
  Set up from cluster utility – set Address and Ports
  Can use more than one
  VE7CC is a common
  Highly Configurable
    User/Spot base, distance, mode, country filters
    Set Alarms and messaging
    Select Rejects
    Link to awards and alerts – LOTW users

## Slide 22: Cluster Spotter Becomes Part Of Logger
CAT CONTROL
DXCC & Awards
CLUSTER Filter
Set Band, Mode and Origin Filters
The Cluster

## Slide 23: How I Operate In My Shack : ICOM (linked To a Panadapter)

## Slide 24: How I Operate in My Shack (Flex)

## Slide 25: Some Concluding Remarks
This is just an introduction, but persistence pays
Tuning around still fun – even better now we have SDR and panoramic displays.
Now have fantastic intelligence and operating tools to catch the DX
Find out what works best for you
Consider joining one of the DX Spots Message Boards (CDXC)